## Slide 1: Evaluating High-Density Swath Bathymetry Sonars Against IHO-S44 Specifications: Ping DSP 3D Sidescan, a case study
David Dodd, IIC Technologies and University of Gothenburg
Paul Kraeutner, Ping DSP Inc.

## Slide 2: Overview
SCAHS S-5B Program
S-44 Standards
Meeting the standards
High resolution Swath Bathymetry systems
HOs approach to SSS hybrids
Example; PING 3D SSS

## Slide 3: Swedish Consortium for Applied Hydrographic Science

## Slide 4: Swedish Consortium for Applied Hydrographic Science
Phase I (2 years):
  IHO/FIG S-5B program
  Cater to:
    industry (MMT and SMA personnel)
    other Nordic region hydrographic organizations
    GU, Chalmers and SU graduate students
    Others
Phase II:
  IHO/FIG S-5A
  GU Marine Science Hydrographic research component

## Slide 5: Consortium Approach
Master’s Course
20-weeks
Four 5-week sections
Section 1 (5 weeks) : Intro to Hydro, Computation Tools, Nautical Science and Meteorology, Remote Sensing, Water levels
Sections 2 and 3 (10 weeks): Theory and applied hydrography intertwined
Section 4 (5 weeks):
  Hydro Projects
  Comprehensive Final Field Project

## Slide 6: S-44 V5 Standards
Special Order and Order 1a
THU – easy with HA GNSS
TVU – main challenge
Target Detection/Resolution – relatively easy, at appropriate speed/ping rate

## Slide 7: S-44 V6 Questionnaire
Open until November 17, 2017 (this Friday)
https://www.surveymonkey.co.uk/r/HSPT_S-44_Q

## Slide 8: Meeting the standards
  Can system meet the standards (TPU)?
  Can system meet target detection (and resolution; i.e. 9 hits/target size - 3 along and 3 across)?
  Prove system can meet the requirements (evaluate over reference surface)
  Surface comparison – does the surface have high enough resolution to effectively evaluate higher resolution systems?
  Positioning must be HA
  Need GNSS heights, not tide
  Keep in mind, uncertainty includes bottom topography
  Prove standards were met:
    Final surface uncertainty (TPU or SD)
    Crosscheck lines

## Slide 9: High-resolution Swath Bathymetry
  SSS Bathymetry
  Swath Bathymetry
  Phase Differencing
  Interferometric
  Angle and range for each pixel (3D SSS)
  Thousands of returns per ping
  High uncertainty in “raw”
  Binning to create smoothed “sounding”

## Slide 10
Taken from: http://www.bathyswath.com/iho-standards

## Slide 11: MB compared to Swath Bathymetry
Angle of return determined through data analysis rather than beam forming

## Slide 12: Hydrographic Office approach to Swath Bathymetry
  No
  Yes, but binned, not “raw”
  Yes, maybe - needs to be approved (show you can meet standards)

## Slide 13: Evaluation of High Resolution Swath Systems
Can the system that created the reference surface achieve the same resolution as the system being evaluated?
Is it valid to evaluate using surfaces created from the same system?

## Slide 14: Ping DSP 3D SSS

## Slide 15: Evaluation
Vancouver Island
Nova Scotia

## Slide 16: 20 m of water

## Slide 17
1A to 6X WD

## Slide 18: NS, NW Cove 10 cm Reference Surfaces
PING: 25.4 density
R2Sonic: 9.5 density
10 cm surface difference, 0.00 m bias, 0.08m SD

## Slide 19
~1000 “beams” for ~100m swath, 6 to 12 m water depth

## Slide 20: Ping X-check line, 10 cm bins, Special Order

## Slide 21: Ping X-check line, 10 cm bins, Order 1A

## Slide 22: Ping L48 JD 053, compared to R2Sonic 0.10, 0.25, 0.50, 1, 2, and 5m surfaces, Special Order

## Slide 23: Ping L48 JD 053, compared to R2Sonic 0.10, 0.25, 0.50, 1, 2, and 5m surfaces, Order 1A

## Slide 24: Ping L48 JD 053, compared to R2Sonic 0.10, 0.25, 0.50, 1, 2, and 5m surfaces, SD

## Slide 25: Coastline
Line 52 South to north. Port side to coastline

## Slide 26: Coastline, Line 52

## Slide 27: Coastline 51
Deep on port side

## Slide 28: Coastline 51
Deep on port side

## Slide 29: Conclusions
High-resolution systems can meet IHO specs
Reference surface from beamforming MB adequate for evaluating high-resolution Swath Bathymetry
Reference surfaces developed from the same system being evaluated provide valid results, but do not take into account any vertical offsets
High resolution SSS swath bathymetry:
  Issues at nadir, especially for Special Order
  Suitable for high-resolution imagery requirements
  Especially useful in shallow harbours and along rugged coastlines