## Slide 1: Hydro17 – Accuracy in Depth Rotterdam, November 15th, 2017
Peter Dugge, Design Lean Navigation, Mission and Charting Systems
Notes: Version 6

## Slide 2: Hydro17 – Accuracy in Depth
Objective
IHO S-44
AUV Design
Error Budget
Total Errors
Conclusion
The hydrographic pros and cons of UUVs compared to surface vessels have been discussed for a while.
A topic which has received less attention so far
is
the considerable gain in accuracy of depth measurements
achievable
when using UUVs rather than surface vessels.
Outline

## Slide 3: Hydro17 – Accuracy in Depth
To design an AUV
which allows to achieve and exceed
the requirements of IHO S-44 Special Order
with a strong focus on depth.
Objective
Objective
IHO S-44
AUV Design
Error Budget
Total Errors
Conclusion

## Slide 4: Hydro17 – Accuracy in Depth
IHO S-44 Maximal Total Horizontal Uncertanity (THU) (95 %)
Objective
IHO S-44
AUV Design
Error Budget
Total Errors
Conclusion
Depth | Order |  | 
 | SO (2 m) | 1a / 1b (5 m + 5 % of depth) | 2 (20 m + 10 % of depth)
5 m | 2.0 m | 5.25 m | n/a
10 m | 2.0 m | 5.5 m | n/a
20 m | 2.0 m | 6.0 m | n/a
50 m | 2.0 m | 7.5 m | n/a
100 m | 2.0 m | 10.0 m | 30 m
200 m | n/a | n/a | 40 m
300 m | n/a | n/a | 50 m
400 m | n/a | n/a | 60 m
500 m | n/a | n/a | 70 m
600 m | n/a | n/a | 80 m

## Slide 5: Hydro17 – Accuracy in Depth
IHO S-44 Maximal Total Vertical Uncertanity (TVU) (95 %)
Objective
IHO S-44
AUV Design
Error Budget
Total Errors
Conclusion
Depth | Order |  | 
 | SO | 1a / 1b | 2
5 m | 0.25 m | 0.50 m | n/a
10 m | 0.26 m | 0.52 m | n/a
20 m | 0.29 m | 0.56 m | n/a
50 m | 0.45 m | 0.82 m | n/a
100 m | 0.79 m | 1.39 m | 2.51 m
200 m | n/a | n/a | 4.71 m
300 m | n/a | n/a | 6.97 m
400 m | n/a | n/a | 9.25 m
500 m | n/a | n/a | 11.54 m
600 m | n/a | n/a | 13.84 m

## Slide 6: Hydro17 – Accuracy in Depth
Components of Navigation System
Objective
IHO S-44
AUV Design
Error Budget
Total Errors
Conclusion
GNSS Receiver
N
Depth
Sound Velocity Sensor
USBL Transponder
Pressure Sensor
INS
DVL
Accuracy 0.07 m (95)
Position

## Slide 7: Hydro17 – Accuracy in Depth
Vertical Error Components, AUV navigation in 200 m depth (𝛿95)
Objective
IHO S-44
AUV Design
Error Budget
Total Errors
Conclusion
Pressure sensor
Tide correction
Density profile
Stagnation pressure
Acceleraton of gravity
Computation of depth with pressure
Surface waves
Installation error of the position between pressure sensor and INS
Atmospheric pressure
Total propagated depth error of navigation
0.07 m
0.1 m
0.019 m
0.0 m
0.0 m
0.0 m
0.0 m
0.005 m
0.012 m
200 m depth
200 m depth, external CTD
20 m depth, 1 m wave hight , 20 m wave length
0.125 m
RTK, commercial SBAS
computation error

## Slide 8: Hydro17 – Accuracy in DepthAccuracy in Depth
Standard Deviation of Vertical Error Components of MBES (σ)
Objective
IHO S-44
AUV Design
Error Budget
Total Errors
Conclusion
Error Source | Alitude over seabed / Beam Angle |  |  | 
 | 20 m / 30° | 50 m / 30° | 20 m / 70° | 50 m / 70°
Acoustic wave detection limit | Not relevant |  |  | 
Sound Velocity Profile | 0.007 m | 0.018 m | 0.051 m | 0.127 m
Roll Error | 0.020 m | 0.050 m | 0.096 m | 0.240 m
Pitch Error | 0.003 m | 0.008 m | 0.003 m | 0.008 m
Installation Error * | 0.005 m | 0.005 m | 0.005 m | 0.005 m
Total propagated MBES Error | 0.022 m | 0.054 m | 0.109 m | 0.272 m
*) of the position between MBES and INS

## Slide 9: Hydro17 – Accuracy in Depth
Total Vertical Error Components of DTM (𝛿95)
Depth | Error source (95) |  |  |  |  | Total propagated vertical error (95)
 | Navigation System |  |  |  | MBES | 
 | Pressure sensor | Density profile | Gravity model | Tide |  | 
5 m | 0.070 m | 0.001 m | 0.001 m | 0.1 m | 0.054 m | 0.134 m
10 m | 0.070 m | 0.001 m | 0.001 m | 0.1 m | 0.107 m | 0.163 m
20 m | 0.070 m | 0.002 m | 0.001 m | 0.1 m | 0.214 m | 0.247 m
50 m | 0.070 m | 0.005 m | 0.003 m | 0.1 m | 0.214 m | 0.247 m
100 m | 0.070 m | 0.010 m | 0.006 m | 0.1 m | 0.214 m | 0.247 m
200 m | 0.070 m | 0.019 m | 0.012 m | 0.1 m | 0.214 m | 0.248 m
300 m | 0.070 m | 0.028 m | 0.018 m | 0.1 m | 0.214 m | 0.249 m
400 m | 0.070 m | 0.037 m | 0.024 m | 0.1 m | 0.214 m | 0.251 m
500 m | 0.070 m | 0.046 m | 0.030 m | 0.1 m | 0.214 m | 0.253 m
600 m | 0.070 m | 0.055 m | 0.036 m | 0.1 m | 0.214 m | 0.255 m
Depth |  |  |  |  |  | 
 | Navigation System |  |  |  | MBES | 
 | Pressure sensor | Density profile | Gravity model | Tide |  | 
5 m | 0.070 m | 0.001 m | 0.001 m | 0.1 m | 0.054 m | 0.134 m
10 m | 0.070 m | 0.001 m | 0.001 m | 0.1 m | 0.107 m | 0.163 m
20 m | 0.070 m | 0.002 m | 0.001 m | 0.1 m | 0.214 m | 0.247 m
50 m | 0.070 m | 0.005 m | 0.003 m | 0.1 m | 0.214 m | 0.247 m
100 m | 0.070 m | 0.010 m | 0.006 m | 0.1 m | 0.214 m | 0.247 m
200 m | 0.070 m | 0.019 m | 0.012 m | 0.1 m | 0.214 m | 0.248 m
300 m | 0.070 m | 0.028 m | 0.018 m | 0.1 m | 0.214 m | 0.249 m
400 m | 0.070 m | 0.037 m | 0.024 m | 0.1 m | 0.214 m | 0.251 m
500 m | 0.070 m | 0.046 m | 0.030 m | 0.1 m | 0.214 m | 0.253 m
600 m | 0.070 m | 0.055 m | 0.036 m | 0.1 m | 0.214 m | 0.255 m
Objective
IHO S-44
AUV Design
Error Budget
Total Errors
Conclusion

## Slide 10: Hydro17 – Accuracy in Depth
Depth | TVU of IHO S-44 Order |  |  | Total propagated vertical error (95)
 | SO | 1a / 1b | 2 | 
5 m | 0.25 m | 0.50 m | n/a | 0.134 m
10 m | 0.26 m | 0.52 m | n/a | 0.163 m
20 m | 0.29 m | 0.56 m | n/a | 0.247 m
50 m | 0.45 m | 0.82 m | n/a | 0.247 m
100 m | 0.79 m | 1.39 m | 2.51 m | 0.247 m
200 m | n/a | n/a | 4.71 m | 0.248 m
300 m | n/a | n/a | 6.97 m | 0.249 m
400 m | n/a | n/a | 9.25 m | 0.251 m
500 m | n/a | n/a | 11.54 m | 0.253 m
600 m | n/a | n/a | 13.84 m | 0.255 m
Depth | TVU of IHO S-44 Order |  |  | 
 | SO | 1a / 1b | 2 | 
5 m | 0.25 m | 0.50 m | n/a | 0.134 m
10 m | 0.26 m | 0.52 m | n/a | 0.163 m
20 m | 0.29 m | 0.56 m | n/a | 0.247 m
50 m | 0.45 m | 0.82 m | n/a | 0.247 m
100 m | 0.79 m | 1.39 m | 2.51 m | 0.247 m
200 m | n/a | n/a | 4.71 m | 0.248 m
300 m | n/a | n/a | 6.97 m | 0.249 m
400 m | n/a | n/a | 9.25 m | 0.251 m
500 m | n/a | n/a | 11.54 m | 0.253 m
600 m | n/a | n/a | 13.84 m | 0.255 m
Comparison of Total Propagated Vertical Error with IHO S-44 TVU
Objective
IHO S-44
AUV Design
Error Budget
Total Errors
Conclusion

## Slide 11: Hydro17 – Accuracy in Depth
Comparison of Total Propagated Vertical Error with IHO S-44 TVU
Objective
IHO S-44
AUV Design
Error Budget
Total Errors
Conclusion
0
0.2
0.4
0.6
0.8
1.0
1.2
1.4
Error (𝛿95) / m
0
10
20
30
40
50
60
70
80
90
100
Water depth / m
Total propagated vertical design error
Maximum TVU to IHO S-44 Order 1a/1b
Maximum TVU to IHO S-44 SO

## Slide 12: Hydro17 – Accuracy in Depth
Conclusion
Thus hydrographic surveyors are offered the opportunity to
establish new survey methods
e.g. to monitor wrecks and off-shore installations with an
unprecedented precision and efficiency.
  This can be achieved by using an AUV with a carefully selected and integrated pressure sensor.
Accuracy requirements of IHO S-44 for depth can be met and exceeded with AUVs.