## Slide 1
A continuum of knowledge from measurements to modelling to explore the future of our seabed resources,
Belgian part of the North Sea
Nathan Terseleer*, Vasilis Hademenos, Tine Missiaen, Jan Stafleu, Dries Van den Eynde, Vera R.M. Van Lancker
*nterseleer@naturalsciences.be
Hydro17 – Connecting 4D Future
16th November 2017

## Slide 2
Started in 1976 (~30x103 m³/yr  >1.7x106 m³/yr in the ‘90s)
Extent and sustainability of the resource?
Effects of extraction on the system?
3D geological model of the resource
link to environmental impact models
 4D Decision Support System
Sand exploited for the industry and beach nourishment
extraction areas
monitoring areas
Marine aggregate extraction in the BCS
… to model (3D)
Concl. & Perspectives
From data…
Introduction
… to model (4D)

## Slide 3
Cores
Seismic profiles
Velocity model: time  depth
Boundaries between
geological units
From measuring…
… to model (3D)
Concl. & Perspectives
Introduction
… to model (4D)
From data…
Holocene
Pleistocene
Tertiary

## Slide 4
3D geological model of the resource
Blocks of information (~200x200x1 m):
lithology
uncertainty
sediment properties
possibly any relevant info
(ecology, chemistry, …)
From measuring… to modelling: the VOXEL model
Concl. & Perspectives
From data…
Introduction
… to model (4D)
… to model (3D)
spatial analysis
(volume calculations, …)
lithological classification
2D lithostratigraphical units
3D interpolation
Stafleu et al., 2011

## Slide 5
EROSION-DEPOSITION  seabed changes…
SUSPENDED LOAD
BED LOAD
TOTAL LOAD
particle diameter
settling velocity
critical shear stress
f
particle density
for different sediment fractions
Hydrodynamics
Sediment Transport
Seabed Morphology
Challenges:
sedimentological resolution  classes, properties
initial conditions (concentrations, available stock vs limitless quantities)
From measuring… to modelling: COHERENS
… to model (3D)
Concl. & Perspectives
From data…
Introduction
… to model (4D)

## Slide 6
Fraction 1
(Clay + Silt)
Layer 1
Layer 2
Layer 3
Fraction 2
(Fine Sand)
Fraction 3
(Medium Sand)
Fraction 4
(Coarse Sand + Gravel)
From measuring… to modelling: VOXEL  COHERENS
The VOXEL model is translated into COHERENS-readable information
… to model (3D)
Concl. & Perspectives
From data…
Introduction
… to model (4D)

## Slide 7
water surface
Fixed layer
erosion
deposition
water column
BATHYMETRY
TERTIARY
FRACTIONS
& PROPERTIES (dp, ρ)
THICKNESS
COHERENS - VOXEL coupling
… to model (3D)
Concl. & Perspectives
From data…
Introduction
… to model (4D)
Bathymetry

## Slide 8
VOXEL-COHERENS: Application (Flemish banks)
extraction areas
monitoring areas
Fraction 1
Fraction 2
Fraction 3
Fraction 4
Particle ø (d50)
50 µm
150 µm
300 µm
600 µm
Single fraction
150 µm
Currents (Spring-Neap cycle):
… to model (3D)
Concl. & Perspectives
From data…
Introduction
… to model (4D)

## Slide 9
VOXEL-COHERENS: Multiple vs Single fractions
Fraction 1
Fraction 2
Fraction 3
Fraction 4
Total (1+2+3+4)
Single Fraction
Suspended load:
Bed load:
… to model (3D)
Concl. & Perspectives
From data…
Introduction
… to model (4D)

## Slide 10
Sediment concentration:
To be used as indicator of a descriptor for the MSFD!
… to model (3D)
Concl. & Perspectives
From data…
Introduction
… to model (4D)
Fraction 1
Fraction 2
Fraction 3
Fraction 4
Total (1+2+3+4)
Single Fraction
Bed shear stress:
Single Fraction
Multiple Fractions
Difference
VOXEL-COHERENS: Multiple vs Single fractions

## Slide 11
 Help producing suitability maps (scenarios)
… to model (3D)
Concl. & Perspectives
From data…
Introduction
… to model (4D)
VOXEL-COHERENS: deposition/erosion pattern
Note the importance of the initialization of the sediments
(inside/outside the VOXEL model area)

## Slide 12
4th Dimension (Time)
 coupling with numerical model
  Importance of IC’s and parameterization
  (resolve the sedimentological resolution)
  Scenarios (sand extraction)
  coupling with a wave model, …
3D VOXEL model:
  coarse sand is limited (>< fine sand!)
  Resource mapping, volume calculations, …
  uncertainty!
Conclusions and perspectives
From measuring to modelling… to society:
  multi-criteria Decision Support System (accounting for uncertainty  confidence limits)
  Suitability maps (user-specific)
  threshold for habitat change, changes in bed shear stress
… to model (3D)
From data…
Introduction
… to model (4D)
Concl. & Perspectives

## Slide 13
THANK YOU
Picture: M. Roche & K. Degrendele @