## Slide 1: The BASE-platform project: Deriving the bathymetry from combined satellite data
Stefan Wiehle, Bernat Martinez, Knut Hartmann, Martin Verlaan, Tim Thornton, SuiWin Hui, Dick Schaap

## Slide 2: Bathymetry
Measurement of waterdepth
Underwater topography
Charts with isobaths for navigation
Rostock
Screenshot: webapp.navionics.com
Notes: Charts can have shoal bias – only shallowest depth mentioned; also thinned data when not required for safe navigation

## Slide 3: Bathymetry
Measurement of waterdepth
Underwater topography
Charts with isobaths for navigation
Bathymetric maps for scientific applications
Screenshot: EMODnet-bathymetry.eu

## Slide 4: Importance of bathymetry
Safety of navigation
Costa Concordia, 13 July 2012 (Source: Camerist, CC BY SA)

## Slide 5: Importance of bathymetry
Safety of navigation
Offshore industries
Lillgrund Wind Farm (Source: Mariusz Paździora, CC BY SA)

## Slide 6: Bathymetry measurement
Most water depths: Survey vessels with echo sounders
Optically shallow waters: LIDAR on planes
Good resolution and accuracy
High costs
Multi-purpose vessel Noortruck in Rostock-Warnemünde during Hydro16
Notes: Multibeam echosounders

## Slide 7: Existing bathymetric data
GEBCO (GEneral Bathymetric Chart of the Oceans)
  Free to use
  Survey data and interpolation
  Available worldwide
  ~900m resolution
EMODnet
  Free to use
  Survey data; GEBCO for gaps
  Limited to European waters
  ~230m resolution
Screenshot: www.gebco.net/
Screenshot: www.emodnet-bathymetry.eu/
Notes: GEBCO: According to a Hydro-Speaker, sometimes it‘s not interpolation, just guessing, as distances between data are too large; some data may be 200 years old
Others: NOAA/NCEI global relief (1‘), US surveys, GEOSS portal (library, but no direct data access),

## Slide 8: BASE-platform project
Create satellite-derived bathymetry (SDB)
Offer these data on web portal
Bathymetry data combining
  Optical SDB
  SAR SDB
  Altimetry SDB
    Crowd-sourced bathymetry (CSB)
  Water level modelling
Horizon2020 project (12/2015-11/2017)

## Slide 9: Satellite-derived bathymetry (SDB)
Different techniques
  Shallow waters: Optical SDB
  Medium depths: SAR SDB
  Deep waters: Altimetry SDB
Benefits
  Satellite data free or cheap
  Fast turnover time
  High data quality using validated methods
Notes: “It has been estimated that a systematic survey of the oceans by ships would take more than 200 years of survey time at a cost of billions of U.S. dollars.” (http://www.gebco.net/general_interest/faq/)

## Slide 10: Optical SDB
Using optical satellite image data of multiple missions (e.g. Sentinel-2)
Physics-based inversion methods to determine water depth from seafloor reflectance intensities in different wavelengths
Depths: 0 to 30m; spatial resolution: 2m to 15m
Example of EOMAP’s Optical SDB product
EOMAP’s Optical SDB processing chain

## Slide 11: SAR SDB
Using SAR data of multiple missions (e.g. Sentinel-1, TerraSAR-X)
Using wave shoaling effect (wave length reduces in shallow water)
Depths: 10 to 100m; spatial resolution: up to ~100m
DLR’s SAR SDB processing chain
Example of DLR’s SAR SDB product

## Slide 12: Altimeter SDB
Using Altimeter satellite data (e.g. Jason-1,Sentinel-3A)
Based on changes in gravity affecting sea surface level caused by large underwater structures (~10km to 200km)
Depths: all non-shallow, spatial resolution: 1 km
Example for isardSAT’s Altimeter SDB product
isardSAT’s Altimeter SDB processing chain

## Slide 13: Crowd-sourced bathymetry (CSB)
Using GPS and depth sounding data collected by ships going about their normal activities
Depths: up to 2km, spatial resolution: 32m
teamSurv’s CSB processing chain
Example for teamSurv’s ship tracks and the resulting bathymetry

## Slide 14: Waterlevel correction
All methods gather depth at time of measurement
Waterlevel simulations allow worldwide correction
Output data in LAT or MSL
Lowest Astronomical Tide relative to Mean Sea Level
Presentation
by Martin Verlaan
on Thu, 14:05h
Notes: Dots are tide gages used for validation.

## Slide 15: Data merging
Combination of the products obtained from each method
Spatial resolution: approx. 15m gridded data
Merged data example and GEBCO data for NW Mauritius
Presentation
by Sandra Gaytán Aguilar
today, 14:25h
Notes: Dots are tide gages used for validation.

## Slide 16: Data accuracy
SDB data compared to CSB and available multibeam surveys
Challenges
  Bathymetry changes over time; data may be deprecated
  Available multibeam data not free of errors (measurement and localization)
Corrections applied to survey data for obvious errors
Method | Optical | SAR | Altimeter | Merge
Depth range (m) | 0-30 | 10-100 | >1000 | All
Mean error (m) | -1,53 | -7,13 | -58,83 | -3,7
URMSE (m) | 1,18 | 11,67 | 88,98 | 4,27

## Slide 17: Trial areas
Data for the trial areas is available for free on our website!

## Slide 18: BASE-platform data portal
Provides easy and fast access to data for end users
Off-the-shelf data
  Already created
  Direct download
  Growing amount of areas
Order data
  Created on request
  All covered areas
  Delivery time: ~3 weeks

## Slide 19: Thanks for your attention!
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No. 687323
Stefan Wiehle
DLR Maritime Safety and Security Lab Bremen
Stefan.Wiehle@dlr.de
+49 421 24420 1863
www.base-platform.com